## Slide 1: Microprocessor Architecture and Internet of Things
Course Code: CET3014B Credits: 3 TH+2 Lab=5

## Slide 2
Course Structure - SY

## Slide 3: CCA LCA

## Slide 4: Unit wise distribution of CCA-70 Marks
LCA-30 Marks

## Slide 5: Syllabus
Module I: Overview of Embedded System and IoT
Module II:Pentium Architecture:
Embedded Systems: Architecture & Characteristics of ES, Types of Embedded systems, Examples of Embedded Systems. Introduction of IoT: Definition and characteristics of IoT, Technical Building blocks of IoT, Device, Communication Technologies, Data, Physical design of IoT, IoT enabling technologies, IoT Issues and Challenges- Planning, Costs and Quality, Security and Privacy, Risks. Example: Smart Home /Smart Agricultural.
Pentium features, Pentium superscalar architecture - Pipelining, Branch prediction, and Instruction and Data caches. The Floating-Point Unit: features, pipeline stages & data types. Pentium programmer's model, register set, System registers, addressing modes and Instruction set.

## Slide 6: Syllabus
Module III:Pentium operating modes:
Pentium Modes of Operation, Pentium Real address mode: Memory organization, Memory segments, segment registers, logical to physical address generation
Protected mode: Segmentation unit support registers, related instructions, segment Memory descriptors, logical to linear address translations.
Module IV:Paging and Protection:
Paging Unit: support registers, related data structures, linear to physical address translation, TLB Protection by segmentation, privilege-levels, rules of inter-privilege level transfer for data and code segments, page level protection.

## Slide 7: Syllabus
Unit 5: Pentium Task Management and Interrupt handling:
Task Management, support registers, related data structures, Task switching. Interrupt and Exception Overview, Sources of Interrupts & exceptions, Exception and Interrupt Vectors, Interrupt Descriptor Table (IDT), IDT Descriptors, Exception- or Interrupt-Handler Procedures

## Slide 8: Learning Resources:
Text Books:
1. The Internet of Things by Hakima Chaouchi Publishers: ISTE and Willey
2. James Antonakos, “The Pentium Microprocessor”, 2004, Pearson Education ISBN – 81-7808-545-3.
Reference Books:
1. Beginning Arduino by Micheal McRoberts Publishers: Technology in Action
2. IoT Fundamental by Devid Hanes Publishers: CISCO
3. Raspberry Pi Cookbook for Python Programmers by Tim Cox Publishers: PACKT
4. The Official Raspberry Pi Project Book
5. Beginning Sensor Networks with Arduino and Raspberry Pi by Charles Bell Publishers: Technology in Action
6. Intel architecture software developer's manual volume 3.
7. Intel architecture software developer's manual volume 1.
8. Intel 64 and IA-32 Architecture’s software developer's manual

## Slide 9
Course Objectives:
By participating in and understanding all facets of this Course a student will be able:
1. Knowledge:
i. To understand the components and techniques used in IoT development environment
ii. To apply the knowledge of fundamentals in IoT for various applications.
iii. To acquire the knowledge of the Pentium processor architectural features, programmer’s model, system registers.
2. Skill:
i. To learn Pentium addressing modes and instruction set for the development of x86/64-bit assembly language programs.
3. Attitude:
i. To describe the role of Memory Management Unit and Privilege levels in protected mode of Pentium processor.
ii. To learn the role of CPU in handling multitasking and processing of interrupts and exceptions in Pentium environment.

## Slide 10
By the end of the course, students will be able to
1. Describe the details of IoT based systems.
2. Demonstrate the use of common IoT platforms and installations.
3. Discuss Pentium architecture and programmer’s model.
4. Apply the Assembly Language Programming skills of Pentium processor.
5. Interpret the demand paging and protection mechanism supported in Pentium Architecture.
6. Demonstrate the concept of Task management and Interrupt handling within the Pentium processor.
Course Outcomes:

## Slide 11: Unit 2: Pentium Architecture
Pentium features, Pentium superscalar architecture - Pipelining, Branch prediction, and Instruction and Data caches.
The Floating-Point Unit: features, pipeline stages & data types.
Pentium programmer's model, register set, System registers,
addressing modes and Instruction set.

## Slide 12: Pentium Processor

## Slide 13: Typical specifications – Only for information
https://www.youtube.com/watch?v=W9Pq32f2rsQ
https://cpu-z.en.uptodown.com/windows/download

## Slide 14: Typical specifications – Only for information
Double Data Rate (DDR)

## Slide 15: Pentium Processor Features
  The Features of Pentium Processor are:
  32bit registers to hold data.
  32 Bit Address Bus and 64 bit data Bus (with Burstable feature)
  Able to be burst. Having the ability to exceed the normal maximum bandwidth for short periods
Address bus decides the memory addressing capacity of processor
Address lines are 32 so memory can be addressed = 2^32 = 4GB
Data bus governs the data handling/processing capacity i.e. maximum size of data can be operated on.
Size of data and address bus should be as large as possible to improve system performance
  Use/role of the above Feature in Pentium Performance

## Slide 16: Pentium Processor Features
  The Features of Pentium Processor are:
  Superscalar – 2 execution pipelines U and V
Any architecture which supports parallel computing through massive pipelining is called as superscalar architecture.
Pipeline implements parallel/overlapped operations in the system and uses all the resources (Buses, ALU, Decoding unit etc.) to the optimum level.
System throughput is improved. Throughput is proportional to frequency in ideal case.(How much data can be transferred from one location to another in a given amount of time. )
Ex. Pipelined Vs Non pipelined operation
https://www.youtube.com/watch?v=AsthZgIS2Lw&list=PLm_MSClsnwm8Dw5nmh8A5E7gO06j1TeIa
  Use/role of the above Feature in Pentium Performance

## Slide 17
Speed up = [nkt] / [kt+ (n-1)t] = nk / [k + n-1] = k / [ 1 + (k-1)/n ]
Speed up ~ k (approx.) as n >> k
n = No. of Operations
K = No. of Pipeline stages
t = Time required at each pipeline stage

## Slide 18: Pentium Processor features
  The Features of Pentium Processor are:
  Separate Code and Data Caches.
    8KB 2-way set associative code cache + TLB (Translation Lookaside buffer)
    8KB 2-way, dual access data cache + TLB
Separate code and data cache balances load on buses so operations are faster.
Memory Management is improved by insertion of TLB – Translation Lookaside buffer between processor and cache.
Cache organizing Techniques:
(i): Direct Mapping (ii) Fully Associative (iii) Set Associative
  Use/role of the above Feature in Pentium Performance

## Slide 19
Only for Understanding

## Slide 20
Only for understanding

## Slide 21
Only for understanding

## Slide 22
Only for understanding

## Slide 23: Pentium Processor features
  The Features of Pentium Processor are:
  2 Prefetch buffers
  A Branch Target Buffer to support Branch prediction logic
  Dynamic Branch Prediction
Branch prediction logic is implemented using Prefetch Buffer and Branch Target Buffer (BTB).
Branch prediction logic reduces branch penalty (in no. of cycles required to flush the pipeline and reload the pipeline with target instructions)
Branch prediction can be Static or Dynamic in nature.
Detailed explanation in later subsection of the unit.
  Use/role of the above Feature in Pentium Performance

## Slide 24: Pentium features
  Pipelined Floating-Point Unit (FPU)
  Improved Instruction Execution Time
  Separate pipeline to process floating point numbers.
  Availability of U and V pipes improves system performance by reducing instruction execution time.
  Use/role of the above Feature in Pentium Performance

## Slide 25: Pentium features
  Write back MESI Data Cache (Modified/Exclusive/Shared/Invalid) Protocol in the
Cache Updation Policies
Write Back
Write Through
  Use/role of the above Feature in Pentium Performance

## Slide 26: Only for understanding

## Slide 27: Only for understanding

## Slide 28: Only for understanding

## Slide 29: Only for understanding

## Slide 30: Pentium features
  System Management Mode
    Provides Power Management mechanisms
  Execution Tracing
  The Pentium 4's execution trace cache stores micro-operations resulting from decoding x86 instructions, providing also the functionality of a micro-operation cache.
  Having this, the next time an instruction is needed, it does not have to be decoded into micro-ops again.

## Slide 31: Pentium features
  Address parity (from the Latin parity, meaning equal or equivalent)

## Slide 32: Pentium features
  Virtual Mode Extension
  The virtual mode extensions are very useful to memory managers and multitasking operating systems.
  Memory managers can primarily benefit by the use of the interrupt redirection bit map to reduce the number of switches to and from protected mode.
https://www.youtube.com/watch?v=o2_iCzS9-ZQ

## Slide 33: https://www.youtube.com/watch?v=o2_iCzS9-ZQ

## Slide 34: Pentium Features
  Internal Parity Checking
  Parity checking for data integrity is done very rigorously in Pentium.
  Pentium checks parity on both the external processor pins, and the internal data structures.
  Cache, buffers, and microcode ROM are all parity checked.
  Additionally, the Pentium supports Functional Redundancy Checking (FRC) [error detection CRC- Cyclic Redundancy Check(CRC) for Error Detection and Correction | Computer Networks]

## Slide 35: Pentium features
  Bus cycle pipeline
    The Pentium is “superscalar pipelined architecture.”
    Superscalar means that the CPU can execute two (or more) instructions per cycle.
    To be more precise: The Pentium can generate the results of two instructions in a single clock cycle.
    The 80486 and Pentium have five-stage pipelines.

## Slide 38
Pentium Super Scalar Architecture - Details

## Slide 39: Pentium Architecture
Components of Pentium Architecture

## Slide 40
Pentium Architecture Detailed view

## Slide 41: On Chip Caches
On Chip two integrated cache – 8Kbyte Data and 8 Kbyte Code Cache
Data Cache Supports MESI (Modify/Exclusive/Shared/Invalid) write back cache consistency Protocol.
Data cache is configurable as Write Through or Write Back on a line-by-line basis.
Code cache is write protected, supports Shared and Invalid stages of MESI Protocol
Cache is organized as a 2-way set associative cache.
Replacement in both the data and code caches is handled by the LRU
( Least Recently used) mechanism.
The data cache can be accessed simultaneously from both pipes, as long as the references are to different cache banks.

## Slide 42
On Chip Caches
Data cache supports the MESI ((Modify/Exclusive/Shared/Invalid) write back cache consistency protocol which requires 2 state bits.
The code cache supports the S and I state only and therefore requires only one state bit.

## Slide 43: TLB - Translation Look Aside Buffer
Each of the caches are accessed with physical addresses and each cache has its own TLB
TLB translates linear address to physical address as required for paging technique
Number of TLB entries = 256

## Slide 44: TLB - Translation Look Aside Buffer
A TLB is organized as a fully associative cache and typically holds 16 to 512 entries. Each TLB entry holds a virtual page number and its corresponding physical page number.
In general, the processor can keep the last several page table entries in a small cache called a translation lookaside buffer (TLB). The processor “looks aside” to find the translation in the TLB before having to access the page table in physical memory. In real programs, the vast majority of accesses hit in the TLB, avoiding the time-consuming page table reads from physical memory.

## Slide 45: Pre-fetch Buffer
To support Branch Prediction Pentium implements Two Pre-fetch Buffers.
One to pre-fetch code in a linear fashion.
Other to pre-fetches code according to the Branch Target Buffer (BTB) so the needed code is almost always pre-fetched before it is needed for execution.
Two independent pairs of line-size (32-byte) pre-fetch buffers operate in conjunction with the branch target buffer.
Only one pre-fetch buffer actively requests pre-fetches at any given time.
Pre-fetches are requested sequentially until a branch instruction is fetched.

## Slide 46
When a branch instruction is fetched, branch target buffer (BTB) predicts whether the branch will be taken or not.
If predicted not taken, pre-fetch requests continue linearly.
On a predicted taken branch the other pre-fetch buffer is enabled and begins to pre-fetch as though the branch was taken.
If a branch is discovered mis-predicted, the instruction pipelines are flushed and prefetching activity starts over.
Example code:
Branching instruction: JNZ
Execution sequence: I0, I1, I2 and I3
Decision at I3:
If condition is true (i.e. ZF = 0) then after I3; I1 and I2 will be executed.
So pipeline must have instructions prefetched as I0 I1 I2 I3 I1 I2 I3 I1 I2 I3 and so on instead of I0 I1 I2 I3 I4, I5 and I6
If condition is false (i.e. ZF = 1) then after I3; I4, I5 and I6 will be executed.
So pipeline must have instructions prefetched as I0 I1 I2 I3 I4, I5 and I6
I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX
Role of Pre-fetch Buffer in Branch Prediction

## Slide 47: Control Unit
  It interprets the instruction word and microcode entry point fed to it by Instruction Decode Unit.
  It handles exceptions, breakpoints and interrupts.
  It controls the integer pipelines and floating point sequences.
  Microcode ROM: Stores microcode sequences.

## Slide 48
Pentium Superscalar Architecture with details of pipeline stages

## Slide 49: Pentium super-scalar architecture
Pentium is capable of executing 2 integer or 2 floating point instructions simultaneously.
This parallel execution is done through two instruction pipelines, the “u” pipe and the “v” pipe.
The u-pipe can execute all integer and floating-point instructions.
The v-pipe can execute simple integer instructions and the FXCH floating-point instruction.
Processors capable of parallel execution of multiple instructions are known as Superscalar machines.

## Slide 50
U pipeline :Capable of handling full instruction set. The u-pipe can execute all integer and floating-point instructions.
V pipeline :Only simple instructions. The v-pipe can execute simple integer instructions and the FXCH floating-point instruction.
Simple Instructions
- are hardwired and do not need microcode, execute in one clock cycle ( Few are listed below)
mov reg, reg/mem/imm
mov mem, reg/imm
alu reg, reg/mem/imm
alu mem, reg/imm
inc reg/mem
dec reg/mem
U and V Pipelines

## Slide 51: Pipelining
Pentium Processor Integer Pipeline with 5 Stages.
Pre fetch (PF):
Decode1:
Decode2:
Execute (EX):
Write Back (WB):

## Slide 52: Pipelining stages Details
Pre fetch (PF)
Instructions are pre fetched from the on-chip instruction cache or memory. ADD AL,BL
Stage 1

## Slide 53: Details of Prefetch Pipeline stages of Pentium
The first stage of the pipeline is the Prefetch (PF) stage in which instructions are prefetched from the on-chip instruction cache or memory.
Because the Pentium processor has separate caches for instructions and data, prefetches do not conflict with data references for access to the cache.
In the PF stage, two independent pairs of 32-byte prefetch buffers operate in conjunction with the branch target buffer.
This allows one prefetch buffer to prefetch instructions sequentially, while the other prefetches according to the branch target buffer predictions

## Slide 54: Prefetch stage
Two pre fetch buffers, 32bytes each.
At a time only one pre fetch buffer is connected to u and v pipes.
The buffer connected to the pipes-
- fetches instructions from code cache sequentially.
The other prefetch buffer
- fetches the instructions as directed by BTB.
Prefetch Buffer1
3/14/2019
35

## Slide 55: Pipelining stages Details
Decode1
The decoders decodes instructions and decides whether they can be paired (control word generator)
Two parallel decoders attempt to decode and issue the next two sequential instructions.
The decoders determine whether one or two instructions can be issued (the instruction pairing rules ).
Stage 2

## Slide 56: Pipelining stages Details
Decode2:
The D1 stage is followed by Decode2 (D2)
Addresses of memory resident operands are calculated (decode control word and generate memory address).
Stage 3

## Slide 57: Pipelining stages Details
Execute (EX): Execute the instructions with data Cache and ALU access
Stage 4

## Slide 58: Pipelining stages Details
Write Back (WB): Modify processor state and complete execution.
Stage 5

## Slide 59: Instruction flow in Pentium pipeline

## Slide 60: Pipeline performance
The maximum throughput is observed with-pipeline
  Every instruction takes exactly one clock cycle to execute
  No or minimum Stalls in pipeline
The number of clock cycles = m+(n-1) where
m = Number of stages in a pipeline
n = Number of instructions in a program
Example: A sequence of 1000 instructions will require 3000 (3*1000) clk cycles on a non pipelined machine and only 1002 (3+1000-1) cycles when pipelined!

## Slide 61
Pipeline stall at decode and execute stage of pipeline

## Slide 62
Prfetch Buffer
I4
I3
I2
I1
I5
Decode2
Decode1
WriteBack
Execution
Execution Unit - creating Stall / bubble
I1, I3, I4 : Simple instructions : 1 CLK Cycle
I2 : Multiplication Instruction : 4CLK Cycles
STALL

## Slide 63
Prfetch Buffer
I4
I3
I2
I1
I5
Decode2
Decode1
WriteBack
Decode2 : Operand fetch, Address generation - creating stall
I1, I2, I4 : Simple instructions : 1 CLK Cycle
I3 : mov ax, buffer[bx+si] : 4CLK Cycles
Execution
STALL

## Slide 64
Prfetch Buffer
I4
I3
I2
I1
I5
Decode2
Decode1
WriteBack
Execution
Decode1 :Instr. Decoding, instruction pairing – creating Stall
I1, I2, I3 : Simple instructions : 1 CLK Cycle
I4 : Xchg : 4CLK Cycles
STALL

## Slide 65
Instruction Pairing Rules

## Slide 66: Instruction Pairing Restrictions /Rules for parallel execution
Both must be simple instructions.
No data dependencies may exist between them.
For floating point instructions pairing:
The first instruction of the pair can be – FLD, FLD st(i), FADD, FMUL, FDIV, FCOM, FTST, FABS, FCHS (Change Sign- Complements sign of ST(0) This operation changes a positive value into a negative value of equal magnitude or vice versa.
The second instruction must be FXCH .
Read after Write Hazard/ Flow dependence Ex. MOV AX, BX MOV DX, AX | Write after Write Hazard/ Output dependence Ex. MOV AX, BX MOV AX, CX

## Slide 67: Instruction Pairing Restrictions /Rules for parallel execution
3. Neither instruction may contain both immediate data and a displacement value (MOV TABLE[SI],7).
4. Prefixed instructions may execute only in U pipeline (MOV ES:[DI],AL).

## Slide 68
Branch Prediction
https://www.youtube.com/watch?v=yk-U6qqeGE0
https://www.youtube.com/watch?v=rJAEGbpRrL4

## Slide 69: Branch Prediction
Performance gain through pipelining can be reduced by the presence of program transfer instructions (such as JMP, CALL, RET and conditional jumps).
They change the sequence causing all the instructions that entered the pipeline after program transfer instruction invalid.
Suppose instruction I3 is a conditional jump to I1 at some other address (target address), then the instructions that entered after I3 is invalid and new sequence beginning with I1 need to be loaded in.
This causes bubbles in pipeline, where no work is done as the pipeline stages are reloaded.
I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX

## Slide 70: Branch Prediction Continued…
In this scheme, a prediction is made with reference to the branch instruction currently in pipeline.
Prediction will be either taken or not taken.
If the prediction turns out to be true, the pipeline will not be flushed and no clock cycles will be lost.
If the prediction turns out to be false, the pipeline is flushed and started over with the correct instruction.
To avoid this problem, the Pentium uses a scheme called Dynamic Branch Prediction.

## Slide 71: Branch Prediction Algorithm

## Slide 72: Branch Prediction
The Pentium processor uses a Branch Target Buffer (BTB) to predict the outcome of branch instructions which minimizes pipeline stalls due to pre-fetch delays.
Algorithm implemented in Pentium for reducing pipeline stalls during execution of jmp instructions
It contains a Branch prediction state machine with four states:
(1) strongly not taken - 00
(2) weakly not taken - 01
(3) weakly taken - 10
(4) strongly taken - 11

## Slide 73: Branch Prediction Algorithm
Two 32 bytes prefetch buffers work with BTB.
One fetches instruction from the current program address and the other buffer is activated when the branch BTB predicts “Taken”.
Initially History bits are 11, when a new target address is placed in BTB.
Whenever branch instruction is encountered, these bits are updated.
If the branch is not taken repetitively then History bits become 00.
BTB is accessed with the address instruction during D1 stage.
If found and the BTB’s prediction is “Taken”, second prefetch buffer becomes active.
If a new branch instruction is encountered (no target address in BTB), the prediction is “Not taken”.

## Slide 74: Example of Branch prediction and subsequent explanation
In this example:
Instruction I3 is branching instruction which will work on the condition based on zero flag.
Condition will be True if ZF = 0, not set and branching will happen; means execution sequence will change from current location (source location i.e. I3) to target location (i.e. I1 or label Bk)
If condition is False i.e. ZF=1; execution sequence will be from current location (I3) to next location (I4) and so on.
When I3 is getting executed first time there is no history associated with it and hence BTB contents will be either 00 or garbage values i.e. no meaning associated with it.
In pipeline at D1 stage, the instruction is decoded and system knows whether it is branching instruction or not.
At Ex stage of pipeline, system comes to know whether branching will take place or not and hence at this stage BTB contents are updated and used for next iteration of the loop.
I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX

## Slide 75
First time execution of branching instruction JNZ Bk
During D1 stage, the JNZ instruction is not known to BTB.
so it’s miss, thus predicts
NO JUMP WOULD BE TAKEN
Accordingly the subsequent instructions I4, I5 … has entered in pipeline.
This is illustrated in next slide.
Example -
I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX

## Slide 76
1
2
3
3
4
1
2
; I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX
3
4
5
7
6
D1
D2
Ex
Control Hazard
T1 CLK
T2 CLK
T5 CLK
U pipe
U pipe
U pipe

## Slide 77
The EX stage (Execute stage) gives feedback to BTB – Branch actually to be taken.
Actions taken further are :
1. BTB is updated as below
2. Pipeline flushed and Instructions I4, I5, I6 and I7 which are entered in pipeline are cleared.
3. Instructions fetched from new address “BK” (I1 and I2 ) in the pre fetch buffer2
4. Pre fetch buffer 2 connected to the pipeline and it behaves as main buffer/ buffer 1 as long as branching takes place.
These actions are illustrated in next slide.
I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX

## Slide 78
3
4
5
7
6
IP
2
1
I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX
Pre fetch Buffer 1
Pre fetch Buffer 2
Flush the pipeline
Connect buffer 2
Bring correct instruction from code cache
First occurrence of JNZ

## Slide 79
1
2
3
3
4
1
2
D1
Prefetch Buffer 1
Prefetch Buffer 1
D2
Ex
U pipe

## Slide 80: Second occurrence of “JNZ” instruction
BTB Hit, Prediction – Branch Strongly taken when reaches Execute Stage
BTB instructs prefetch stage to fetch instructions from addr. “BK”
One buffer prefetches instructions from target ie. I1 and I2
Second buffer prefetches instructions I4, I5 and so on.
During last iteration, when ZF=1 then branching will not happen and new instructions will be readily available in one of the buffer hence the correct buffer will be attached to U and V pipe.
I0 MOV SI, addr
Bk : I1 INC SI
I2 DEC CX
I3 JNZ BK
I4 ADD AX,BX
I5 INC AX
I6 MOV [SI] , AX

## Slide 81: BTB Example
Consider the following loop for computing prime numbers:
for(k=i+prime;k<=SIZE;k+=prime)
flags[k]=FALSE;
A popular compiler generates the following assembly code:
(prime is allocated to ecx, k is allocated to edx, and al contains the value FALSE)
inner_loop:
mov byte ptr flags[edx],al
add edx,ecx
cmp edx, SIZE
jle inner_loop
Each iteration of this loop will execute in 6 clocks on the Intel486 CPU.
On the Pentium processor, the mov is paired with the add; the cmp with the jle. With branch prediction,each loop iteration executes in 2 clocks.

## Slide 82
Floating Point Unit Details

## Slide 83: Floating Point Unit
The floating-point unit (FPU) of the Pentium processor is integrated with the integer unit on the same chip.
It is heavily pipelined.
The Pentium processor FPU is implemented with
8 pipeline stages.
First 5 stages are shared with Integer Unit.
The integer instruction uses the fifth stage as writeback.

## Slide 84: Floating Point instructions in the pipeline
FP instruction does not get paired with integer instruction
Two FP instructions can be paired only if
  1. FXCH instruction is the second instruction in the pair.
  2. The first instruction of the pair can be – FLD, FLD st(i), All forms of FADD, FMUL, FDIV, FCOM, FUCOM, FTST, FABS, FCHS
  3. The instructions which do not follow a and b always are issued to “u” pipe singly.

## Slide 85: Floating Point Unit (FPU) – Key Points
FPU of Pentium is Integrated with Integer Unit
FPU is Heavily Pipelined Unit
Able to accept one floating point instruction / clock
Able to accept two floating point instruction every clock - But – One instruction out of it must be EXCHANGE

## Slide 86: Floating Point Unit Pipeline Stages
FPU Works with 8 Pipeline stages
It shares first 5 stages of Integer Unit
PF- Prefetch
D1- Instruction Decode
D2- Address Generation
EX- Memory & Register Read
X1- FP Execute Stage 1
X2- Execute Stage 2
WF- Write Result
ER- Error Reporting

## Slide 87: 8 pipeline stages of FPU with Bypass 1 and Bypass 2
PF - Prefetch
D1 - Instruction Decode
D2 - Address generation
EX - Memory and register read : conversion of FP data to external memory format and memory write.
5. X1 - Floating-Point Execute stage one : conversion of external memory format to internal FP data format and write operand to FP register file; bypass 1 (send data back to EX stage)
6. X2 - Floating-Point Execute stage two
7. WF - Perform rounding and write floating-point result to register file; bypass 2 (send data back to EX stage)
8. ER- Error Reporting/Update Status Word

## Slide 88: Floating Point Pipeline with Bypass

## Slide 89: FPU Register File

## Slide 90: Impact of Bypass Technique
With bypass technique, the result from the previous instruction is about to be written to the register file, is made directly available as an operand to any succeeding instruction that needs it.
Two Types: Bypass 1 and Bypass 2

## Slide 91: Bypass 1 Details
Bypass 1, the X1 stage register file write port and the EX stage register file read port.
With bypass 1, the result of a floating-point load (that writes to the register file in the X1 stage) can bypass the X1 stage write and be sent directly to the operand fetch stage or EX stage of the next instruction..

## Slide 92: BYPASS 1 Example
Bypass connects the output of X1 stage to the input of EX stage
e.g - FLD ST
      FMUL ST
The above instructions use ST as an operand.
With byapss1, the data from FLD is made available as an input operand to FMUL before it is written into the floating point register file.
This prevents the pipeline from stalling and decreases number of clk cycles.
No of clk cycles taken by 8087 to execute FMUL instruction are 130 whereas, Pentium takes only 1 clk cycle to perform the same operation!

## Slide 93: Bypass 2 Details
Bypass the WF stage register file write port and the EX stage register file read port.
With bypass 2, the result of any arithmetic operation can bypass the WF stage write to the register file, and be sent directly to the desired execution unit as an operand for the next instruction.

## Slide 94: BYPASS 2 Example
Bypass between WF stage and EX stage where the result of an arithmetic instruction is made available to the next instruction.
e.g. – FADD NUM
FMUL NUM1
The first instruction does
  Top of stack 🡸 Top of stack + NUM
  It does this in WF stage of the pipeline.
The next instruction “FMUL NUM1” does
  Top of stack 🡸 Top of stack X NUM1
With bypass2, even before the result is written to top of the stack in register file, the result is directly forwarded to the next instruction “FMUL NUM1” in its EX stage.

## Slide 95
System Level Architecture Overview Programmers Model

## Slide 96: System Level Architecture
Programmers Model
  Set of Register
  Data structures
  Instructions

## Slide 97: Register categories
  General Purpose Registers
  Flag Registers
  Index Registers
  Debug Registers
  Pointer Registers
  Segment Registers
  Memory Management Registers
  Control Registers
General purpose registers
  EAX,EBX,ECX,EDX
Index Registers
  ESI,EDI
Pointer Registers
  ESP,EBP
Segment Registers
  DS,CS,SS,ES,FS,GS
Flag Register
  EFLAGS
Memory Management Registers
  GDTR, LDTR, TR, IDTR
Control Registers
  CR0,CR1,CR2,CR3, CR4
Debug Registers
  DR0, DR1, DR2, DR3, DR4, DR5, DR6, DR7

## Slide 98: Register Categories
General purpose registers
  EAX,EBX,ECX,EDX
Index Registers
  ESI,EDI
Pointer Registers
  ESP,EBP
Segment Registers
  DS,CS,SS,ES,FS,GS
Flag Register
  EFLAGS
Memory Management Registers
  GDTR, LDTR, TR, IDTR
Control Registers
  CR0,CR1,CR2,CR3, CR4
Debug Registers
  DR0, DR1, DR2, DR3, DR4, DR5, DR6, DR7

## Slide 99
Application Registers

## Slide 100: Segment Registers
Six Segment Registers
Each with 16 bit capacity
Used to hold distinct content
  Code
  Data
  Stack

## Slide 101: EFLAG Registers
Carry Flag
Parity Flag
Auxiliary Flag
Zero
Flag
Sign
Flag
Direction
Flag
Overflow
Flag
Interrupt
Flag
Trap
Flag

## Slide 102
IOPL – Indicates the I/O Privilege level of Currently running program / Task 00-01 10 11
CPL <= IOPL to access IO Address Space
Nested Task – control chaining of Interrupted and called tasks
Resume Flag – controls the processors response to “Instruction Breakpoint” Condition.
VM – to set Virtual 8086 mode.
AC- Alignment Check– when set enable alignment checking of memory references (along with AM flag in CR0)
EFLAG Registers

## Slide 103
Virtual Interrupt Flag (VIF) – contains a Virtual image of IF flag, works along with VIP bit.
Virtual Interrupt Pending (VIP) – Indicated that an interrupt is pending works along with VIF
“To Consider these flags, either VME or PVI flag of CR4 need to be set and IOPL < 3”
Identification –ability of program to set/clear this bit indicates support for the CPUID instruction
EFLAG Registers

## Slide 104
EFLAG Registers

## Slide 105: Control Registers

## Slide 106
Memory Management Registers

## Slide 107: Memory Management Registers
GDTR – Global Descriptor Table Register
IDTR – Interrupt Descriptor Table Register
LDTR- Local Descriptor Table Register
TR – Task Register

## Slide 108: GDTR
Global Descriptor Table
Segment Descriptor - n
Segment Descriptor
Segment Descriptor
Segment Descriptor
Segment Descriptor - 2
Segment Descriptor- 1
0
GDTR
Hold linear address of Base of Global Descriptor Table
The GDTR register holds the 32-bit base address and 16-bit table limit for the GDT.
The base address specifies the linear address of byte 0 of the GDT
the table limit specifies the number of bytes in the table.
32 bit BA
16 bit Table Limit
Base Address=32 Bit
2^16=64KB=65536
2^13=8192
8192*8=64KB
64 Bit

## Slide 109: IDTR
IDTR holds the linear address of the base of the IDT
32-bit base address and 16-bit table limit for the IDT.
Base address specifies the linear address of byte 0 of the IDT
Table limit specifies the number of bytes in the table.
External interrupts, software interrupts, and exceptions are handled through the interrupt descriptor table (IDT).
IDT contains a collection of gate descriptors, to access interrupt and exception handlers.
LIDT & SIDT instructions load and store the IDTR register, respectively

## Slide 110: LDTR
The linear address of the LDT is contained in the LDT register (LDTR).
LDT contain entries called segment descriptors which provides the base address of a segment and access rights, type, and usage information.
LDTR register holds the 16-bit segment selector, 32-bit base address, 16-bit segment limit, and descriptor attributes for the LDT.
Base address specifies the linear address of byte 0 of the LDT segment. The segment limit specifies the number of bytes in the segment.
LLDT and SLDT instructions load and store the segment selector part of the LDTR register.

## Slide 111: Task Register
Task register holds
  16-bit segment selector
  32-bit base address
  16-bit segment limit,
  Descriptor attributes for the TSS of the current task.
Base address specifies the linear address of byte 0 of the TSS
Segment limit specifies the number of bytes in the TSS.
LTR and STR instructions load and store the segment selector part of the task register

## Slide 112: Control Registers
Control Registers (CR0, CR1, CR2, CR3, and CR4) determine operating mode of the processor and the characteristics of the currently executing task

## Slide 113: Control Registers
CR0 – Defines paging, protection, extension type, task switched etc.
CR1 – Reserved
CR2 - Contains the Page Fault Linear Address
CR3 - Contains Physical address of base of Paging (PDBR) Mechanism, MSB 20 bits are specified and LSB 12 are assumed 0.
CR4 - Additional control bits

## Slide 114
PG – Paging Bit 31 of CR0 – for enabling and disabling paging mechanism
PE- Protection Enable bit 0 of CR0 – enables protected mode
VME- Virtual 8086 Modes Extension – bit 0 of CR4- enable interrupt and exception handling in virtual 8086 mode
Important bits of Control Registers

## Slide 115: Debug Registers
DR0 through DR7 are available for debugging and performance monitoring.
Holds address of memory or IO location called Breakpoints
A debug exception occurs (#DB) when a memory or IO access is made to a breakpoint address.

## Slide 116: Data Types
Byte, word, doubleword and quadword are principal data types i.e 8 bit, 16, 32 and 64 bits.
In case of any size, the lowest address is refereed always. Higher address are only used when upper byte/word/double/quad is accessed separately from the lower or when individual bytes are being accessed.

## Slide 117: Data Types
Bytes,
Words,
Doublewords
Quadwords storage in Memory

## Slide 118: Data Types
Integer - All operations assume a two's complement representation. MSB is used as sign bit. The value of an 8-bit integer is from –128 to +127; a 16-bit integer from –32,768 to +32,767; a 32-bit integer from –231 to +231 –1
Ordinal: An unsigned binary number contained the value of an 8-bit ordinal is from 0 to 255; a 16-bit ordinal from 0 to 65,535; a 32-bit ordinal from 0 to 2^32 – 1. This is sometimes referred to as an unsigned integer.
BCD Integer: A representation of a binary-coded decimal (BCD) digit in the range 0 through 9. Unpacked decimal numbers are stored as unsigned byte quantities.
Packed BCD Integer: A representation of binary-coded decimal digits, each in the range 0 to 9. One digit is stored in each half-byte, two digits in each byte. The digit in bits 4 to 7 is more significant than the digit in bits 0 to 3. Values 0 to 9 are valid for a digit.

## Slide 119: Data Types
Near Pointer: A 32-bit effective address. A near pointer is an offset within a segment. Near pointers are used for all pointers in a flat memory model, or for references within a segment in a segmented model.
Far Pointer: A 48-bit logical address consisting of a 16-bit segment selector and a 32-bit offset. Far pointers are used in a segmented memory model to access other segments.
Bit Field: A contiguous sequence of bits. A bit field can begin at any bit position of any byte and can contain up to 32 bits.
Bit String: A contiguous sequence of bits. A bit string can begin at any bit position of any byte and can contain up to 23^2– 1 bits.
Byte String: A contiguous sequence of bytes, words, or doublewords. A string can contain from zero to 2^32 – 1 bytes (4 gigabytes).

## Slide 120: Addressing Modes

## Slide 121: Addressing Mode with Example

## Slide 122: Addressing mode with example

## Slide 123: Addressing Modes
Register Mode – operand is located in one of the general purpose register
  Ex – MOV EAX, EBX
Immediate Mode- operand is included in instruction itself.
  Ex – SHL Pattern, 2 or
Memory Mode need effective address calculations.
EA = Base + (Index*Scaling)+ Displacement
MOV AX, 45H

## Slide 124: Few Important Rules
The ESP register cannot be used as an index register.
When the ESP or EBP register is used as the base, the SS segment is the default selection. In all other cases, the DS segment is the default selection.
The base, index, and displacement components can be used in any combination; any of these components can be null. A scale factor can be used only when an index also is used.
The displacement alone indicates the offset of the operand. This form of addressing is used to access a statically allocated scalar operand.

## Slide 125: Few important Rules
BASE + DISPLACEMENT
A register and a displacement can be used together for two distinct purposes:
Index into an array when the element size is not 2, 4, or 8 bytes. The displacement component encodes the offset of the beginning of the array. The register holds the results of a calculation to determine the offset to a specific element within the array.
Access a field of a record. The base register holds the address of the beginning of the record, while the displacement is an offset to the field.

## Slide 126: Few important Rules
(INDEX * SCALE) + DISPLACEMENT
This combination is an efficient way to index into a static array when the element size is 2, 4, or 8 bytes. The displacement addresses the beginning of the array, the index register holds the subscript of the desired array element, and the processor automatically converts the subscript into an index by applying the scaling factor.
BASE + INDEX + DISPLACEMENT
Two registers used together support either a two-dimensional array (the displacement holds the address of the beginning of the array) or one of several instances of an array of records (the displacement is an offset to a field within the record).
BASE + (INDEX * SCALE) + DISPLACEMENT
This combination provides efficient indexing of a two-dimensional array when the elements of the array are 2, 4, or 8 bytes in size

## Slide 127: Few important Rules

## Slide 128: Addressing Modes
Section .data
value DW 0
sum DD 0
marks TIMES 10 DW 0
message DB ’The grade is:’,0
char1 DB ?
The assembler assigns contiguous (offset addresses) memory space for the variables.
It uses the same ordering of variables that is present in the source code.
Finding the offset value of a variable is counting the number of bytes allocated to all the variables preceding it.
For example, the offset value of marks is 6 because value and sum are allocated 2 and 4 bytes, respectively.

## Slide 129: Addressing mode with example
1/7/2023

## Slide 130: Addressing mode with example

## Slide 131: Addressing mode with example

## Slide 132: Addressing mode with example

## Slide 133
Instruction Set

## Slide 134: Data Transfer Instructions
MOV Move
XCHG Exchange
PUSH/PUSHF Push onto stack
POP /POPF Pop off of stack
SAHF store AH into flags
IN Read from a port
OUT Write to a port
LDS Load far pointer using DS
LES Load far pointer using ES
LEA Load effective address
XLAT Exchange byte/word

## Slide 135: Data Transfer Instructions
Additional Pentium instructions:
  PUSHA Push ALL registers
  POPA Pop ALL registers
  INS Input string from port
  OUTS Output string from port
  LFS Load far pointer using FS
  LGS Load far pointer using GS
  LSS Load far pointer using SS
  MOVSX Move and sign extend
  MOVZX Move and zero extend
  PUSHD/PUSHAD/PUSHFD Push DOUBLE registers onto stack
  POPD/POPAD /POPFD Pop DOUBLE registers from stack
  BSWAP Byte swap
  MOV Move to/from control register

## Slide 136: Binary Arithmetic Instructions
ADD Integer add
ADC Add with carry
SUB Subtract
SBB Subtract with borrow
IMUL Signed multiply
MUL Unsigned multiply
IDIV Signed divide
DIV Unsigned divide
INC Increment
DEC Decrement
NEG Negate
CMP Compare

## Slide 137: Binary Arithmetic Instructions
Additional Pentium instructions:
  CDQ convert double word to quad word
  CWDE convert word to double word
  CMPXCHG compare and exchange
  XADD exchange and add
  CMPXCHG8B compare and exchange 8bytes

## Slide 138: Bit Manipulation Instructions
AND and
OR or
XOR Exclusive or
NOT Not
SAR Shift arithmetic right
SHR Shift logical right
SAL/SHL Shift arithmetic left/Shift logical left
SHRD Shift right double
SHLD Shift left double
ROR Rotate right
ROL Rotate left
RCR Rotate through carry right
RCL Rotate through carry left
TEST test byte/word

## Slide 139: Bit manipulation Instructions
Additional Pentium instructions:
  BSF Bit scan forward
  BSR Bit scan reverse
  BT Bit test
  BTC Bit test and complement
  BTR Bit test and reset
  BTS Bit test and set
  SHLD shift left double precision
  SHRD shift right double precision
  SETcc set byte on condition

## Slide 140: Control Transfer Instructions
JMP Jump
JE/JZ Jump if equal/Jump if zero
JA/JNBE Jump if above/Jump if not below or equal
JL/JNGE Jump if less/Jump if not greater or equal
JC Jump if carry
JO Jump if overflow
JS Jump if sign (negative)
RET Return
IRET Return from interrupt
INT Software interrupt
INTO Interrupt on overflow
LOOPZ/LOOPE Loop with ECX and zero/Loop with ECX and equal

## Slide 141: String Instructions
  MOVS/MOVSB Move string/Move byte string
  CMPS/CMPSB Compare string
  SCAS/SCASB Scan string/Scan byte string
  LODS/LODSB Load string/Load byte string
  STOS/STOSB Store string/Store byte string
  REP Repeat while ECX not zero
  REPE/REPZ Repeat while equal/Repeat while zero
  REPNE/REPNZ Repeat while not equal/Repeat while not zero

## Slide 142: Flag Control Instructions
STC Set carry flag
CLC Clear the carry flag
CMC Complement the carry flag
CLD Clear the direction flag
STD Set direction flag
LAHF Load flags into AH register
SAHF Store AH register into flags
STI Set interrupt flag
CLI Clear the interrupt flag

## Slide 143
Additional Pentium instructions:
  BOUND Detect value out of range
  ENTER High-level procedure entry
  LEAVE High-level procedure exit
  IRETD interrupt return
  JECXZ jump if ECX is zero

## Slide 144: Protected Mode Instructions
LGDT Load global descriptor table (GDT) register
SGDT Store global descriptor table (GDT) register
LLDT Load local descriptor table (LDT) register
SLDT Store local descriptor table (LDT) register
LTR Load task register
STR Store task register
LIDT Load interrupt descriptor table (IDT) register
SIDT Store interrupt descriptor table (IDT) register
MOV Load and store control registers
MOV Load and store debug registers

## Slide 145: Protected Mode Instructions
LMSW Load machine status word
SMSW Store machine status word
CLTS Clear the task-switched flag
ARPL Adjust requested privilege level
LAR Load access rights
LSL Load segment limit
VERR Verify segment for reading
VERW Verify segment for writing

## Slide 146
  INVD Invalidate cache, no writeback
  WBINVD Invalidate cache, with writeback
  INVLPG Invalidate TLB Entry
  LOCK (prefix) Lock Bus
  HLT Halt processor
  RSM Return from system management mode (SSM)
  RDMSR Read model-specific register
  WRMSR Write model-specific register
  RDPMC Read performance monitoring counters
  RDTSC Read time stamp counter
  CPUID Processor Identification
Additional Pentium instructions